## Slide 1
Is the compound a sesquiterpene (nC=15, nH=24, nC=C>=1)?
Compound with metadata (SMILES, kOH, C*) and mechanism name
Is the compound explicit in CRACMM? (identified w/ canonical SMILES or info from SMILES)
yes
Is the compound [(C10H16) or (C10H18O1)] and nC=C =1?
Lumped Species
α-pinene and other terpenes with one double bond (nC=C) (API)
Is the compound [(C10H16) or (C10H18O1)] and nC=C >=2?
Lumped Species
δ-limonene and other diene-terpenes (LIM)
Lumped Species
Sesquiterpenes (SESQ)
no
no
no
no
Explicit Species
Acetaldehyde (ACD)
Acetylene (ACE)
Acetone (ACT)
Benzene (BEN)
Methane (ECH4)
Ethanol (EOH)
Ethene (ETE)
Ethylene glycol (ETEG)
Ethane (ETH)
Formaldehyde (HCHO)
Isoprene (ISO)
Methanol (MOH)
Formic acid (ORA1)
Methyl hydrogen peroxide (OP1)
Methyl ethyl ketone (MEK)
Methyl vinyl ketone (MVK)
Acrolein (ACRO)
1,3 butadiene (BDE13)
Toluene (TOL)
Styrene (STY)
Ethylbenzene (EBZ)
Naphthalene (NAPH)
Phenol (PHEN)
CRACMM3M only: Methyl iodide (CH3I)
yes
yes
yes
Terpenes
Is the compound slow reacting (kOH<3.5×10-13 cm3 molec-1 s-1)?
Lumped Species
Slow reacting species with lifetime > ~1 month (SLOWROC)
yes
no
Is the species a ROC species?
yes
no
Species is unknown (UNKSMILES) or not ROC (UNKCRACMM)
Is the compound 2 carbons with more than one aldehyde?
Lumped Species
Glyoxal and similar species like glycoaldehyde (GLY)
yes
no
Is the compound 3 carbons with 2 alcohol groups?
Semiexplicit species
Propylene glycol and other 3 carbon dialcohols (PROG)
yes
no
Explicit and Semiexplicit
CRACMMv3.0 Emissions Mapping, Updated 6/8/2026
Is the compound a furan?
yes
Lumped Species
Furans and other dienes (FURAN)
no
Continue to Schematic A
Functional updates to the cracmm mapper for CRACMM3 highlighted in yellow.
The mapper can map to CRACMM3 or CRACMM3M. The only difference in CRACMM3M is explicit CH3I.

## Slide 2
Does the compound have 1 aromatic benzene ring?
Go to schematic C for species without aromatic rings
no
no
SVOC of various O:C and lower volatility aromatic species
Go to schematic B for species with an aromatic ring
yes
no
Does the compound have log10C*<(-0.5)?
Lumped Species: SVOCs of C* 0.1 µg/m3
If O:C > 0.45: Species with O:C ~0.6 (A/VROCN2OXY6)
Else if O:C > 0.2: Species with O:C ~0.3 (A/VROCN2OXY3)
Else if O:C > 0.05: Species with O:C ~0.1 (A/VROCN2OXY1)
Else: Alkane-like species (ROCN1ALK)
Does the compound have log10C*<1.5?
Lumped Species: SVOCs of C* 10 µg/m3
If O:C > 0.2: Species with O:C ~0.3 (A/VROCP1OXY3)
Else if O:C > 0.05: Species with O:C ~0.1 (A/VROCP1OXY1)
Else: Alkane-like species (A/VROCP1ALK)
Lumped Species: SVOCs of C* 1 µg/m3
If O:C > 0.3: Species with O:C ~0.4 (A/VROCP0OXY4)
Else if O:C > 0.1: Species with O:C ~0.2 (A/VROCP0OXY2)
Else: Alkane-like species (A/VROCP0ALK)
Does the compound have log10C*<0.5?
no
no
yes
yes
yes
Does the compound have log10C*<2.5?
Lumped Species: SVOCs of C* 100 µg/m3
If O:C > 0.1: Species with O:C ~0.2 (A/VROCP2OXY2)
Else: Alkane-like species (A/VROCP2ALK)
yes
Does the compound have log10C*<(-1.5)?
Lumped Species: SVOCs of C* 0.01 µg/m3
If O:C > 0.6: Species with O:C ~ 0.8 (A/VROCN2OXY8)
Else if O:C > 0.3: Species with O:C ~ 0.4 (A/VROCN2OXY4)
Else If O:C > 0.1: Species with O:C ~ 0.2 (A/VROCN2OXY2)
Else: Alkane-like species (A/VROCN2ALK)
no
yes
Schematic A
CRACMMv3.0 Emissions Mapping, Updated 6/8/2026

## Slide 3
Is the compound an aromatic aldehyde (naldehyde>1)?
Lumped Species
Benzaldehyde and aromatic aldehydes (BALD)
Is the compound nalcohol>=2?
Lumped Species
Methylcatechol (MCT)
Lumped Species
Cresols (CSL)
Is the compound and nalcohol>=1?
Is the compound another single-ring aromatic?
Lumped Species
Xylenes and other reactive aromatics (XYL)
no
no
no
no
yes
yes
yes
yes
Single-ring aromatics
One aromatic ring (nbenzene>0)
Does the compound have log10C*<6.5?
Lumped Species
Aromatic-like IVOCs of highest volatility (VROCP6ARO)
Lumped Species
Aromatic-like IVOCs of intermediate volatility (VROCP5ARO)
Does the compound have log10C*<5.5?
no
yes
yes
Schematic B
CRACMMv3.0 Emissions Mapping, Updated 6/8/2026

## Slide 4
No aromatic rings (nbenzene=0)
Does the compound have multiple double bonds (nC=C >=2) ?
Lumped Species
Larger dienes and furans (FURAN)
Is the compound an internal olefin (id via bond location)?
Lumped Species
Internal alkene (OLI)
Is the compound a terminal olefin (id via bond location)?
Lumped Species
Terminal alkene (OLT)
Does the compound have ncarbonyl>=2 and nC=C =1?
Lumped Species
Unsaturated dicarbonyls (DCB1)
Is the compound nC=4, naldehyde=1, nC=C =1?
Lumped Species
Methacrolein and crotonaldehyde (MACR)
Is the compound nC=C =1, naldehyde>=1?
Lumped Species
Unsaturated aldehydes (UALD)
Compounds with C=C
yes
yes
yes
yes
yes
yes
no
no
no
no
no
Does the compound have nC=C >=1 and log10C*<6.5?
Lumped Species
Aromatic-like IVOCs of highest volatility (VROCP6ARO)
Lumped Species
Aromatic-like IVOCs of intermediate volatility (VROCP5ARO)
Does the compound have nC=C >=1 and log10C*<5.5?
no
yes
yes
no
Does the compound have log10C*<4.5?
Lumped Species
If O:C > 0.4: oxygenated IVOCs and siloxanes (VROCIOXY)
Else if O:C > 0.1: Oxygenated IVOC of lower volatility (VROCP4OXY2)
Else: Alkane-like IVOCs of lower volatility (VROCP4ALK)
Does the compound have log10C*<6.5?
Lumped Species
If O:C > 0.2: oxygenated IVOCs and siloxanes (VROCIOXY)
Else if O:C > 0.05: Oxygenated IVOC of highest volatility (VROCP6OXY1)
Alkane-like IVOCs of highest volatility (VROCP6ALK)
Lumped Species
If O:C > 0.2: oxygenated IVOCs and siloxanes (VROCIOXY)
Else if O:C > 0.05: Oxygenated IVOC of intermed. vol. (VROCP5OXY1)
Alkane-like IVOCs of intermediate volatility (VROCP5ALK)
Does the compound have log10C*<5.5?
no
no
yes
yes
yes
Does the compound have log10C*<3.5?
Lumped Species
If O:C > 0.4: oxygenated IVOCs and siloxanes (VROCIOXY)
Else if O:C > 0.1: Oxygenated IVOC of lowest volatility (A/VROCP3OXY2)
Else: Alkane-like IVOCs of lowest volatility (A/VROCP3ALK)
no
yes
IVOCs without aromaticity
no
no
Does the compound have (log10C*<6.5 and an ether/carbamate) or Si?
Lumped Species
Oxygenated IVOCs and siloxanes typical of VCP sources (VROCIOXY)
yes
no
Continue to schematic D
Schematic C
CRACMMv3.0 Emissions Mapping, Updated 6/8/2026

## Slide 5
Unknown (UNKCRACMM)
The CRACMM3 emission mapper includes some other updates for robustness, specifically more use of canonical smiles. These updates are not expected to change any previous CRACMM2 mappings. Some species can exist in a gas (V) or aerosol (A) phase. The python mapper includes an optional argument to label a species as gas or particle if two phases are possible . The user must specify the phase as input to the mapper (it is not diagnosed). The phase can be calculated based on C* and organic aerosol concentration outside the mapper.
C* are always in µg m-3 in this diagram.
Unknowns may be of 3 types:
UNKKOH: unknown kOH (correct by specifying better surrogate).
UNKSMILES: unknown SMILES (correct by specifying better surrogate).
UNKCRACMM: unknown in mapping. All ROC species eventually get classified by kOH, but species that do not have any carbon atoms or are elemental carbon do not get mapped.
CRACMM2 documentation: Skipper et al. (2024) https://doi.org/10.5194/acp-24-12903-2024);
CRACMM1 documentation: Pye et al. (2023) https://doi.org/10.5194/acp-23-5043-2023 and Place et al. (2023) https://doi.org/10.5194/acp-23-9173-2023
RACM2 SI: Goliff et al. (2013) https://ars.els-cdn.com/content/image/1-s2.0-S1352231012011065-mmc1.pdf
Is species slow reacting
(kOH < 3.4×10-12 cm3 molec-1 s-1)?
Lumped Species
Slow reacting species (HC3)
Is the species intermediate reacting (kOH >= 3.4×10-12 and
kOH <= 6.8×10-12 cm3 molec-1 s-1)?
Lumped Species
Moderately reacting species (HC5)
Is the compound fast reacting
(kOH > 6.8×10-12 cm3 molec-1 s-1)?
Lumped Species
Fast reacting species (HC10)
yes
yes
yes
no
no
“Alkanes”
no
Oxygenated Species
Does the compound have naldehyde>=1 and nketone>=1?
Lumped Species
methylglyoxal and similar, kOH =1.5×10-11 cm3 molec-1 s-1 (MGLY)
Is the compound an aldehyde (naldehyde>=1)?
Lumped Species
higher aldehydes (C>3), kOH =1.98×10-11 cm3 molec-1 s-1 (ALD)
Is the compound a hydroxy ketone (nalcohol>=1 and nketone>=1)?
Lumped Species
hydroxy ketone, kOH =3.0×10-12 cm3 molec-1 s-1 (HKET)
Lumped Species
higher organic peroxides, kOH =6.4×10-12 cm3 molec-1 s-1 (OP2)
Is the compound a peroxide (nperoxide>=1)?
Is the compound a ketone (nketone>=1)?
Lumped Species
all other ketones, kOH =2.9×10-12 cm3 molec-1 s-1 (KET)
Is the compound an alcohol (nalcohol>=1)?
Lumped Species
C3 and higher alcohols, kOH =1.3e-12 (ROH)
Lumped Species
organic nitrates, kOH =2.2×10-12 cm3 molec-1 s-1 (ONIT)
Is the compound a nitrate (nnitrate>=1)?
Is the compound an acid
(nacid>=1 )?
Lumped Species
acetic and higher acids, kOH =6.5×10-13 cm3 molec-1 s-1 (ORA2)
no
no
no
no
no
no
no
yes
yes
yes
yes
yes
yes
yes
yes
no
Schematic D
CRACMMv3.0 Emissions Mapping, Updated 6/8/2026